First Slide Example
Robotic Merit Badge Session #1
- Merit Badge Counselor: Maurice Ling
- July 6, 2015
- http://bsatroop675.org

---
Default Example
Agenda
- Class Overview
  - Schedule
  - Materials for the Class
  - Robotics Merit Badge Requirements
  - Competition
- Safety Working in Robotics
- Introduction to Your Robot Brain (Dagu Micromagician)
- Programming
  - Development Tips
  - Exercises
- Assignment to work on before Session #2

---
Schedule
Class Dates	Topics
7/6	Introduction, Material Distribution, Programming
7/20	Programming, Electronics, Competition Specifications, / Design
8/3	Design Review, Electronics
8/17	Pre-competition Preparation, / Advanced Topics
8/31	Robotics Showcase/Competition

---
Computer Setup
- Review Class Reference Guide.
  - Arduino IDE Installation
  - USB Driver Installation
  - Github account
    - Fork https://github.com/mcli/RoboticsMB
    - Clone your RoboticsMB project
    - Launch Git Shell or Terminal
    - Setup upstream project:
    - Synchronize upstream project (when needed)
git remote add upstream https://github.com/mcli/RoboticsMB.git
git fetch upstream
git checkout master
git merge upstream/master

---
GitHub
- GitHub is a source code control service, based on the “git” utility
- I will use it to look at your programs to monitor your progress
- Commit and synchronize your code to make it available in your GitHub repository.
- Commit your code when you reach a stable point in development to checkpoint your changes.
- You can also synchronize with my project to get any class examples or utilities.
- Fork https://github.com/mcli/RoboticsMB and make it your upstream project (See Preparing for the First Session).

---
Material Inventory
- Carrying Case
- Tadpole Robot Kit
  - The Tadpole is only the starting point for your robot design.
  - You will be modifying it to achieve your own design goals.
- 4 AAA NiMH batteries
- Engineering notebook
- Merit Badge Booklet
- Merit Badge Workbook

---
Scout-Provided Materials
- Blue Card signed by Scoutmaster
- Computer with Arduino development environment installed
- USB-A to mini-USB Cable
- AAA NiMH battery charger
- Small phillips screw driver
- Pen/Pencil for taking notes

---
Other Useful Items
- Sony/Universal Remote Control
- Electric Multimeter to measure Voltage and Resistance
- Solder and Soldering Iron

---
Merit Badge Requirements
All Requirements are listed in the Workbook and Merit Badge Booklet and cover:
- Safety
- Robotics in industry
- General Knowledge
- Demonstration
- Competitions
- Careers
  Complete the workbook on your own for Merit Badge Counselor review/check-off

---
Robotics Showcase Competition
- Gives you objectives for your robot design.
- You may optionally work together with one other scout as a team.
- Have fun.
- More details will be announced at the 2nd Session

---
Safety Working with Robotics

---
Safety Working with Robotics
- Have a clean work area
- Electrical Circuits
  - Always disconnect power when modifying circuits.
- Electro-static discharge
- Precautions when cutting material

---
Introduction to Your Robot Brain
- The MicroMagician Controller
  - Atmega 328 microprocessor
  - Digital and Analog pins (I/O)
  - Power in/out -3.3V vs 5V
  - Motor driver and connections
  - Accelerometer
  - IR receiver

---
Analog Vs Digital Signals
- Analog signals are continuous with many values between minimum and maximum. e.g. a sine wave. Typically used for sensor processing.
- Digital signals are discrete. e.g. 0 or 1. Typically used to turn something on or off.

---
Arduino IDE Setup
- Board Configuration
  - Arduino Pro or Pro Mini
  - Atmega 328 (3.3V, 8MHz)
- Serial Port
  - Windows – COM3
  - Mac – (port that does not say bluetooth)

---
Development Tips
- Using the IDE to compile and upload programs (“sketches”)
- Using the Reference: Help → Reference
  - setup() - Runs once
  - loop() - Gets called continuously
  - ; (semicolon)
  - Data Types
  - = (assignment) vs == (equal to)
- All code must be within a function
- Utilizing libraries (microM Library)

---
Programming Exercises - Blink
- Load the Blink program from Examples → 01.Basics
- Save it in your sketchbook
- Compile it and upload it to the MicroMagician Board
void setup() {
  // initialize digital pin 13 as an output.
  pinMode(13, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
  digitalWrite(13, HIGH); // turn the LED on (HIGH is the voltage level)
  delay(1000); // wait for a second
  digitalWrite(13, LOW); // turn the LED off by making the voltage LOW
  delay(1000); // wait for a second
}

---
Programming Exercises – Modifying Blink
- Save the pin number (13) in an “int” variable and replace all instances of “13” with the variable. e.g. int ledPin=13;
- Modify the program to generate the SOS signal – 3 short, 3 long, 3 short, pause, then repeat.
- Save as BlinkSOS and github commit.
- Revise the program to add 2 function, shortBlinks() and longBlinks(), to generate the SOS signal to make the program shorter and more readable.
- Save and github commit.
- Revise the program to use one function instead of two (combine shortBlinks() and longBlinks() into one)
- Save and github commit and sync.

---
Programming Exercises – Blink SOS – 2 functions
void setup()
{
 // same setup as before
}
void shortBlinks()
{
  for (int I = 0; I < 3)
  {
    // call digitalWrite/delay here
  }
}
// define void longBlinks() here, similar to shortBlinks()
void loop()
{
   shortBlinks();
   longBlinks();
   shortBlinks();
  delay(1000);
}

---
Programming Exercises – Blink SOS in 1 function
void setup()
{
 // same setup as before
}
void blinks(int length)
{
// have an if/then statement to check if length is negative,
       // delay with the absolute value of length and don't blink
// call digitalWrite and delay(length) here
}
// define void longBlinks() here, similar to shortBlinks()
void loop()
{
  // call blinks here with different parameters
}

---
Programming Exercises – Accelerometer
- Load the MicroM example “impact”: Files →libraries → microM → impact
- Open the Serial Monitor: Tools → Serial Monitor
- Run program, then tap the board lightly from different directions to see the delta values change
- Save the program into your sketches
- Modify the program to print the x, y, and z axis readings (not the delta readings)
- Turn the board in different directions and observe the readings.

---
Programming Exercises – Accelerometer
#include <microM.h>
void setup()
{
  microM.Setup(); // this must be called first in your setup function
  microM.sensitivity=50; // if your robot vibrates or moves over a rough surface
        // then increase this value to prevent false triggering
  microM.devibrate=50; // depends on the construction of your robot. Increase
        // the value if you get additional readings after initial impact
  Serial.begin(9600); // initialize serial monitor
  Serial.println("Ready");
}

---
Programming Exercises – Accelerometer
void loop()
{
  microM.Impact(); // function must be called at least once every 2mS to
        //work accurately
  If (microM.magnitude>0) // display results of impact
  {
    Serial.println("");
    Serial.print("\tMagnitude:");
    Serial.print(microM.magnitude);
    Serial.print("\tDelta X:");
    Serial.print(microM.deltx);
    Serial.print("\tDelta Y:");
    Serial.print(microM.delty);
    Serial.print("\tDelta Z:");
    Serial.println(microM.deltz);
    Serial.println("");
    microM.magnitude=0; // prevents display repeating the same values
  }

---
Assignment
- Finish Class Exercises
- Commit and sync your programming exercises to your GitHub RoboticsMB project.
- Put together your tadpole robot following the instructions at instructables.com. Note that our Tadpole kit does not contain the bumper switches.
- Follow the tutorials at RocketBrandStudios to program and calibrate the motors.
- If you have Sony or universal remote control, use the microM → IR Receiver project to determine what codes correspond to which buttons on your remote. Write the button names/functions and the corresponding codes in a table in your engineering notebook. See if you can control your robot using the IR remote control.