First Slide Example
Robotic Merit Badge Session #2
- Merit Badge Counselor: Maurice Ling
- July 20, 2015
- http://bsatroop675.org

---
Default Example
Agenda
- Homework Review
- Competition Details
- Electronics
  - Hooking up the Obstacle Sensor
- Programming
  - Reading the Obstacle Sensor inputs
  - Exercises
- Session #2 Homework

---
Homework Review
- Programming with Functions
- Functions with arguments
- Calibrating Motors
- Using GitHub

---
Programming with Functions
void setup()
{
 // same setup as before
}
void shortBlinks()
{
  for (int i = 0; i < 3; i++)
  {
    // call digitalWrite/delay here set pin HIGH, then LOW
  }
}
// define void longBlinks() here, similar to shortBlinks()
void loop()
{
   shortBlinks();
   longBlinks();
   shortBlinks();
  delay(1000);
}

---
Functions with Arguments
const int ledPin=13;
 // same setup() as before
void blinks(int length)
{
for (int i = 0; i < 3; i++)	// Loop three times
  {
digitalWrite(ledPin, HIGH); // turn on
      delay(length);
digitalWrite(ledPin, LOW); // turn off
delay(length);
 }
}
void loop()
{
const int longLength=1000;
const int shortLength=500;
blinks(shortLength);
blinks(longLength);
blinks(shortLength);
delay(longLength); // pause before repeating sequence
}

---
GitHub Client

---
Calibrating The Motors
- Connections to Motor A Output and Motor B Output
- microM.motors(leftSpeed,rightSpeed,leftBrake,rightBrake);
- Figuring out the Right and Left Motors
- Making your robot go straight.

---
Looking Under the Hood at the microM Library
- microM.h – Header file defines the microM C++ class and methods (functions) you can use.
- microM.cpp – The implementation of the C++ class
void MicroM::Motors(int leftSpeed, int rightSpeed, byte leftBrake, byte rightBrake)
{
pinMode(7,OUTPUT);
PinMode(8,OUTPUT);
if(leftBrake!=0)
{
digitalWrite(5,1);
digitalWrite(7,1);
}
else
{
If (leftSpeed==0)
{
digitalWrite(5,0);
digitalWrite(7,0);
}
I f(leftSpeed>0)
{
analogWrite(5,leftSpeed);
digitalWrite(7,0);
}
If (leftSpeed<0)
{
leftSpeed+=255;
analogWrite(5,leftSpeed);
digitalWrite(7,1);
}
}
...

---
Announcing the 2015 Troop 675
Robotics Competition!

---
Robotic Uranium Carry
- Objective: Transport radioactive uranium capsule from one reactor to another.
- Uranium capsule will take the form of a ping pong ball
- Begin and end with a human-controlled segment to load and unload the capsule.
- Carefully navigate a maze autonomously
- Option to team up with another scout

---
Competition Scoring
- Points scored for each portion completed
- Bonus points for time completed within 5 minutes
- Bonus Creativity points
- Bonus Design points
- Penalty points
- Parent Judge panel

---
Obstacle Sensor

---
Obstacle Sensor Hookup
TBD

---
Programming Exercises
TBD

---
Session #2 Homework
- Complete class exercises
- In your notebook, capture the design for the competition
  - How to load/unload the capsule
  - How to carry the capsule
  - Sketch the logic required to navigate maze
- Program your robot to implement your maze navigation logic
- Robotics MB Workbook:
  - Section 3
  - Section 4 a, b

---
Introduction to Your Robot Brain
- The MicroMagician Controller
  - Atmega 328 microprocessor
  - Digital and Analog pins (I/O)
  - Power in/out -3.3V vs 5V
  - Motor driver and connections
  - Accelerometer
  - IR receiver

---
Analog Vs Digital Signals
- Analog signals are continuous with many values between minimum and maximum. e.g. a sine wave. Typically used for sensor processing.
- Digital signals are discrete. e.g. 0 or 1. Typically used to turn something on or off.

---
Arduino IDE Setup
- Board Configuration
  - Arduino Pro or Pro Mini
  - Atmega 328 (3.3V, 8MHz)
- Serial Port
  - Windows – COM3
  - Mac – (port that does not say bluetooth)

---
Development Tips
- Using the IDE to compile and upload programs (“sketches”)
- Using the Reference: Help → Reference
  - setup() - Runs once
  - loop() - Gets called continuously
  - ; (semicolon)
  - Data Types
  - = (assignment) vs == (equal to)
- All code must be within a function
- Utilizing libraries (microM Library)

---
Programming Exercises - Blink
- Load the Blink program from Examples → 01.Basics
- Save it in your sketchbook
- Compile it and upload it to the MicroMagician Board
void setup() {
  // initialize digital pin 13 as an output.
  pinMode(13, OUTPUT);
}
// the loop function runs over and over again forever
void loop() {
  digitalWrite(13, HIGH); // turn the LED on (HIGH is the voltage level)
  delay(1000); // wait for a second
  digitalWrite(13, LOW); // turn the LED off by making the voltage LOW
  delay(1000); // wait for a second
}

---
Programming Exercises – Modifying Blink
- Save the pin number (13) in an “int” variable and replace all instances of “13” with the variable. e.g. int ledPin=13;
- Modify the program to generate the SOS signal – 3 short, 3 long, 3 short, pause, then repeat.
- Save as BlinkSOS and github commit.
- Revise the program to add 2 function, shortBlinks() and longBlinks(), to generate the SOS signal to make the program shorter and more readable.
- Save and github commit.
- Revise the program to use one function instead of two (combine shortBlinks() and longBlinks() into one)
- Save and github commit and sync.

---
Programming Exercises – Blink SOS – 2 functions
void setup()
{
 // same setup as before
}
void shortBlinks()
{
  for (int I = 0; I < 3)
  {
    // call digitalWrite/delay here
  }
}
// define void longBlinks() here, similar to shortBlinks()
void loop()
{
   shortBlinks();
   longBlinks();
   shortBlinks();
  delay(1000);
}

---
Programming Exercises – Blink SOS in 1 function
void setup()
{
 // same setup as before
}
void blinks(int length)
{
// have an if/then statement to check if length is negative,
       // delay with the absolute value of length and don't blink
// call digitalWrite and delay(length) here
}
// define void longBlinks() here, similar to shortBlinks()
void loop()
{
  // call blinks here with different parameters
}

---
Programming Exercises – Accelerometer
- Load the MicroM example “impact”: Files →libraries → microM → impact
- Open the Serial Monitor: Tools → Serial Monitor
- Run program, then tap the board lightly from different directions to see the delta values change
- Save the program into your sketches
- Modify the program to print the x, y, and z axis readings (not the delta readings)
- Turn the board in different directions and observe the readings.

---
Programming Exercises – Accelerometer
#include <microM.h>
void setup()
{
  microM.Setup(); // this must be called first in your setup function
  microM.sensitivity=50; // if your robot vibrates or moves over a rough surface
        // then increase this value to prevent false triggering
  microM.devibrate=50; // depends on the construction of your robot. Increase
        // the value if you get additional readings after initial impact
  Serial.begin(9600); // initialize serial monitor
  Serial.println("Ready");
}

---
Programming Exercises – Accelerometer
void loop()
{
  microM.Impact(); // function must be called at least once every 2mS to
        //work accurately
  If (microM.magnitude>0) // display results of impact
  {
    Serial.println("");
    Serial.print("\tMagnitude:");
    Serial.print(microM.magnitude);
    Serial.print("\tDelta X:");
    Serial.print(microM.deltx);
    Serial.print("\tDelta Y:");
    Serial.print(microM.delty);
    Serial.print("\tDelta Z:");
    Serial.println(microM.deltz);
    Serial.println("");
    microM.magnitude=0; // prevents display repeating the same values
  }

---
Assignment
- Finish Class Exercises
- Commit and sync your programming exercises to your GitHub RoboticsMB project.
- Put together your tadpole robot following the instructions at instructables.com. Note that our Tadpole kit does not contain the bumper switches.
- Follow the tutorials at RocketBrandStudios to program and calibrate the motors.
- If you have Sony or universal remote control, use the microM → IR Receiver project to determine what codes correspond to which buttons on your remote. Write the button names/functions and the corresponding codes in a table in your engineering notebook. See if you can control your robot using the IR remote control.